## Slide 1: Chapter 17
Rigid Body Dynamics

## Slide 2: fig_06_006
Unconstrained Motion:
3 Equations for x, y, rotation

## Slide 3: fig_06_006
Describe the constraint(s) with an Equation
Constrained Motion:
The system no longer has all Degrees of freedom

## Slide 4: Center of Mass

## Slide 5
Chapter 17 Inertial Dynamics
Frame
Free-Body
Constraint equations. You must have as many equations as unknowns. COUNT!

## Slide 6
EQUATIONS OF MOTION:
ROTATION ABOUT A FIXED AXIS
Today’s Objectives:
Analyze the planar kinetics of a rigid body undergoing rotational motion.
Notes: 6

## Slide 7
Pure Rotation
The crank on the oil-pump rig undergoes rotation about a fixed axis, caused by the driving torque, M, from a motor.
If the motor exerts a constant torque M on the crank, does the crank turn at a constant angular velocity?
As the crank turns, a dynamic reaction is produced at the pin. This reaction is a function of angular velocity, angular acceleration, and the orientation of the crank.
Pin at the center of rotation.

## Slide 8
When a rigid body undergoes only translation, all the particles of the body have the same acceleration so aG = a and a = 0. The equations of motion become:
Note that, if it makes the problem easier, the moment equation can be applied about another point instead of the mass center. For example, if point A is chosen,
MA = (m aG ) d .
EQUATIONS OF MOTION: TRANSLATION
(Section 17.3)
 Fx = m(aG)x
 Fy = m(aG)y
 MG = 0
Notes: 8

## Slide 9
EQUATIONS OF ROTATIONAL MOTION
We need to determine the effects caused by the moments of an external force system.
The moment about point P can be written as:
 (ri  Fi) +  Mi = r  maG + IG
 Mp = (Mk)p
where r = x i + y j and  Mp is the resultant moment about P due to all the external forces.
The term (Mk)p is called the kinetic moment about point P.
Notes: 9

## Slide 10
If point P coincides with the mass center G, this equation reduces to the scalar equation of MG = IG  .
In words: the resultant (summation) moment about the mass center due to all the external forces is equal to the moment of inertia about G times the angular acceleration of the body.
Thus, three independent scalar equations of motion may be used to describe the general planar motion of a rigid body. These equations are:
EQUATIONS OF ROTATIONAL MOTION (continued)
 Fx = m(aG)x
 Fy = m(aG)y
and  MG = IG or  Mp =  (Mk)p
Notes: 10

## Slide 11
EQUATIONS OF MOTION: ROTATION ABOUT A FIXED AXIS
 Fn = m (aG)n = m rG w2
 Ft = m (aG)t = m rG a
 MG = IG a
Since the body experiences an angular acceleration, its inertia creates a moment of magnitude, Iga, equal to the moment of the external forces about point G. Thus, the scalar equations of motion can be stated as:
When a rigid body rotates about a fixed axis perpendicular to the plane of the body at point O, the body’s center of gravity G moves in a circular path of radius rG. Thus, the acceleration of point G can be represented by a tangential component (aG)t = rG a and a normal component (aG)n = rG w2.

## Slide 12
EQUATIONS OF MOTION (continued)
Fn = m (aG)n = m rG w2
Ft = m (aG)t = m rG a
MO = IO a
From the parallel axis theorem, IO = IG + m(rG)2, therefore the term in parentheses represents IO.
Note that the MG moment equation may be replaced by a moment summation about any arbitrary point. Summing the moment about the center of rotation O yields
MO = IGa + rG m (aG) t = [IG + m(rG)2] a
Consequently, we can write the three equations of motion for the body as:

## Slide 13: Chapter 17.5
General Plane Motion
=
=
Remember Rel. Motion Kinematics:

## Slide 14: fig_06_002
fig_06_002
Plane Motion
3 equations:
S Forces_x
Forces_y
Moments about G

## Slide 15: Chapter 17.5
Constraints
Constraint Equations are required whenever there are more independent variables than degrees of Freedom.
Example:
We choose two coordinates:
y downward
q counterclockwise.
The constraint eq. is y = -R*q

## Slide 16: fig_06_001
fig_06_001

## Slide 17: fig_06_001
fig_06_001

## Slide 18: fig_06_002
fig_06_002
Plane Motion

## Slide 19: fig_06_002
fig_06_002
Plane Motion
3 equations:
S Forces_x
Forces_y
Moments about G

## Slide 20: fig_06_002
fig_06_002
Plane Motion
3 equations:
S Forces_x
Forces_y
Moments about G

## Slide 21: fig_06_005
fig_06_005
Parallel Axes Theorem

## Slide 22: fig_06_005
fig_06_005
Parallel Axes Theorem
Pure rotation about fixed point P

## Slide 23: fig_06_005
Radius of Gyration
Pure rotation about center G
Inertia is concentrated at radius k

## Slide 24: fig_06_005
2 Equations:

## Slide 25
Today’s Objectives :
Students will be able to:
Analyze the kinematics of a rigid body undergoing planar translation or rotation about a fixed axis.
In-Class Activities :
• Check Homework
• Reading Quiz
• Applications
• Types of Rigid-Body Motion
• Planar Translation
• Rotation About a Fixed Axis
• Concept Quiz
• Group Problem Solving
• Attention Quiz
PLANAR RIGID BODY MOTION: TRANSLATION & ROTATION

## Slide 26
APPLICATIONS
Passengers on this amusement ride are subjected to curvilinear translation since the vehicle moves in a circular path but they always remains upright.
Does each passenger feel the same acceleration?
If the angular motion of the rotating arms is known, how can we determine the velocity and acceleration experienced by the passengers? Why would we want to know these values?

## Slide 27
APPLICATIONS (continued)
Gears, pulleys and cams, which rotate about fixed axes, are often used in machinery to generate motion and transmit forces. The angular motion of these components must be understood to properly design the system.
To do this design, we need to relate the angular motions of contacting bodies that rotate about different fixed axes. How is this different than the analyses we did in earlier chapters?

## Slide 28
RIGID BODY MOTION (Section 16.1)
We will now start to study rigid body motion. The analysis will be limited to planar motion.
For example, in the design of gears, cams, and links in machinery or mechanisms, rotation of the body is an important aspect in the analysis of motion.
There are cases where an object cannot be treated as a particle. In these cases the size or shape of the body must be considered. Rotation of the body about its center of mass requires a different approach.
A body is said to undergo planar motion when all parts of the body move along paths equidistant from a fixed plane.

## Slide 29
PLANAR RIGID BODY MOTION
There are three types of planar rigid body motion.

## Slide 30
PLANAR RIGID BODY MOTION (continued)
Translation: Translation occurs if every line segment on the body remains parallel to its original direction during the motion. When all points move along straight lines, the motion is called rectilinear translation. When the paths of motion are curved lines, the motion is called curvilinear translation.

## Slide 31
Rotation about a fixed axis: In this case, all the particles of the body, except those on the axis of rotation, move along circular paths in planes perpendicular to the axis of rotation.
PLANAR RIGID BODY MOTION (continued)
General plane motion: In this case, the body undergoes both translation and rotation. Translation occurs within a plane and rotation occurs about an axis perpendicular to this plane.

## Slide 32
The piston undergoes rectilinear translation since it is constrained to slide in a straight line.
The connecting rod undergoes curvilinear translation, since it will remain horizontal as it moves along a circular path.
The wheel and crank undergo rotation about a fixed axis. In this case, both axes of rotation are at the location of the pins and perpendicular to the plane of the figure.
An example of bodies undergoing the three types of motion is shown in this mechanism.
The connecting rod undergoes general plane motion, as it will both translate and rotate.
PLANAR RIGID BODY MOTION (continued)

## Slide 33
RIGID-BODY MOTION: TRANSLATION
(Section 16.2)
The positions of two points A and B on a translating body can be related by
rB = rA + rB/A
where rA & rB are the absolute position vectors defined from the fixed x-y coordinate system, and rB/A is the relative-position vector between B and A.
Note, all points in a rigid body subjected to translation move with the same velocity and acceleration.
The velocity at B is vB = vA+ drB/A/dt .
Now drB/A/dt = 0 since rB/A is constant. So, vB = vA, and by following similar logic, aB = aA.

## Slide 34
RIGID-BODY MOTION: ROTATION ABOUT A FIXED AXIS (Section 16.3)
The change in angular position, d, is called the angular displacement, with units of either radians or revolutions. They are related by
1 revolution = (2) radians
When a body rotates about a fixed axis, any point P in the body travels along a circular path. The angular position of P is defined by q.
Angular velocity, , is obtained by taking the time derivative of angular displacement:
 = d/dt (rad/s) +
Similarly, angular acceleration is
 = d2/dt2 = d/dt or  = (d/d) + rad/s2

## Slide 35
If the angular acceleration of the body is constant, a = aC, the equations for angular velocity and acceleration can be integrated to yield the set of algebraic equations below.
w = w0 + aC t
q = q0 + w0 t + 0.5 aC t2
w2 = (w0)2 + 2aC (q – q0)
q0 and w0 are the initial values of the body’s angular position and angular velocity. Note these equations are very similar to the constant acceleration relations developed for the rectilinear motion of a particle.
RIGID-BODY MOTION: ROTATION ABOUT A FIXED AXIS (continued)

## Slide 36
The magnitude of the velocity of P is equal to wr (the text provides the derivation). The velocity’s direction is tangent to the circular path of P.
In the vector formulation, the magnitude and direction of v can be determined from the cross product of w and rp . Here rp is a vector from any point on the axis of rotation to P.
v = w × rp = w × r
The direction of v is determined by the right-hand rule.
RIGID-BODY ROTATION: VELOCITY OF POINT P

## Slide 37
The acceleration of P is expressed in terms of its normal (an) and tangential (at) components.
In scalar form, these are at = a r and an = w2 r.
The tangential component, at, represents the time rate of change in the velocity's magnitude. It is directed tangent to the path of motion.
The normal component, an, represents the time rate of change in the velocity’s direction. It is directed toward the center of the circular path.
RIGID-BODY ROTATION: ACCELERATION OF POINT P

## Slide 38
Using the vector formulation, the acceleration of P can also be defined by differentiating the velocity.
a = dv/dt = dw/dt × rP + w × drP/dt
= a × rP + w × (w × rP)
It can be shown that this equation reduces to
a = a × r – w2r = at + an
RIGID-BODY ROTATION: ACCELERATION OF POINT P (continued)
The magnitude of the acceleration vector is a = (at)2 + (an)2

## Slide 39
ROTATION ABOUT A FIXED AXIS: PROCEDURE
• Establish a sign convention along the axis of rotation.
• Alternatively, the vector form of the equations can be used (with i, j, k components).
v = w × rP = w × r
a = at + an = a × rP + w × (w × rP) = a × r – w2r
• If a is constant, use the equations for constant angular acceleration.
• If a relationship is known between any two of the variables (a, w, q, or t), the other variables can be determined from the equations: w = dq/dt a = dw/dt a dq = w dw
• To determine the motion of a point, the scalar equations v = w r, at = a r, an = w2r , and a = (at)2 + (an)2 can be used.

## Slide 40
EXAMPLE
Given: The motor gives the blade an angular acceleration  = 20 e-0.6t rad/s2, where t is in seconds. The initial conditions are that
when t = 0, the blade is at rest.
Find: The velocity and acceleration of the tip P of one of the blades when t =3 s. How many revolutions has the blade turned in 3 s ?
Plan:
1) Determine the angular velocity and displacement of the blade using kinematics of angular motion.
2) The magnitudes of the velocity and acceleration of point P can be determined from the scalar equations of motion for a point on a rotating body. Why scalar?

## Slide 41
EXAMPLE (continued)
Solution:
1) Since the angular acceleration is given as a function of time,  = 20 e-0.6t rad/s2 , the angular velocity and displacement can be found by integration.
=   dt = 20  e-0.6t dt
w = e-0.6t
20
(-0.6)
 =  w dt
 =  e-0.6t dt = e-0.6t
20
(-0.6)
20
(-0.6)2
Angular displacement
Also , when t = 3 s,  = 20 e-0.6(3) b= 3.306 rad/s2
when t = 3 s,
w = -5.510 rad/s
when t = 3 s,
 = 9.183 rad
= 1.46 rev.

## Slide 42
2) The velocity of point P on the the fan, at a radius of 1.75 ft, is determined as
vP = w r = (5.510)(1.75) = 9.64 ft/s
The magnitude of the acceleration of P is determined by
aP = (an)2 + (at)2 = (53.13)2 + (5.786)2 = 53.4 ft/s2
EXAMPLE (continued)
The normal and tangential components of acceleration of point P are calculated as
an = (w)2 r = (5.510)2 (1.75) = 53.13 ft/s2
at = a r = (3.306)(1.75) = 5.786 ft/s2

## Slide 43
GROUP PROBLEM SOLVING
Given: Starting from rest when gear A is given a constant angular acceleration, aA = 4.5 rad/s2. The cord is wrapped around pulley D which is rigidly attached to gear B.
Find: The velocity of cylinder C and
the distance it travels in 3 seconds.
1) The angular acceleration of gear B (and pulley D) can be related to aA.
2) The acceleration of cylinder C can be determined by using the equations for motion of a point on a rotating body since (at)D at point P is the same as ac.
3) The velocity and distance of C can be found by using the constant acceleration equations.
Plan:

## Slide 44
GROUP PROBLEM SOLVING (continued)
Solution:
Since gear B and pulley D turn together, aD = aB = 1.5 rad/s2
1) Gear A and B will have the same speed and tangential component of acceleration at the point where they mesh. Thus,
at = aArA = aBrB  (4.5)(75) = aB(225)  aB = 1.5 rad/s2
2) Assuming the cord attached to pulley D is inextensible and does not slip, the velocity and acceleration of cylinder C will be the same as the velocity and tangential component of acceleration along the pulley D:
aC = (at)D = aD rD = (1.5)(0.125) = 0.1875 m/s2

## Slide 45
3) Since aA is constant, aD and aC will be constant. The constant acceleration equation for rectilinear motion can be used to determine the velocity and displacement of cylinder C when t = 3 s (s0= v0 = 0):
vc = v0 + aC t = 0 + 0.1875 (3) = 0.563 m/s
GROUP PROBLEM SOLVING (continued)
sc = s0 + v0 t + (0.5) aC t2
= 0 + 0 + (0.5) 0.1875 (3)2 = 0.844 m